## Slide 1: How to make switchport as a Trunk, Access or Desirable port in VLAN
Prepared by: Fahad Burhan Ahmad

## Slide 2
Access Port just transfer the data to specific VLAN

## Slide 6: VLAN Port membership

## Slide 7: VLAN 10 UIIT Configuration Commands (Single Port)
Switch(config)#vlan 10
Switch(config-vlan)#int fa 0/1
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 10
Switch(config-if)#exit
Switch(config)#exit
Switch#show run

## Slide 8: VLAN 20 UIMS Configuration Commands (multiple Port)
Switch>enable
Switch#conf ter
Switch(config)#vlan 20
Switch(config-vlan)#int range fa 0/22-23
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#switchport access vlan 20
Switch(config-if-range)#exit
Switch(config)#exit
Switch#show run or show vlan

## Slide 9: creating Trunk Port
To make port trunk
Switch>enable
Switch#conf ter
Switch(config)#int fa 0/24
Switch(config-if)#switchport mode trunk
Switch#show vlan
Switch#show int trunk

## Slide 10: Delete VLAN
To delete interfaces manually from VLAN
Switch(config)#interface range fastEthernet 0/1-10
Switch(config-if-range)#no switchport access vlan 10
Switch(config-if-range)#exit

## Slide 12: Important Note
To get traffic of all VLAN’s *
Create all vlans same like you created in other switches
Vlan 10
Vlan 20
Vlan 30

## Slide 13: Thanks for Watching
Repeat the steps until you learn